## Slide 4
Motor is connected to the “M4” port will supply the movement of the robot and play right wheel role. That is why we should configure in this way.

## Slide 5
Motor is connected to the “M1” port will supply the movement of the robot and play left wheel role. That is why we should configure in this way.

## Slide 6
Motor is connected to the “M3” port will supply the power to scissor lift mechanism to rise or drop. That is why we should configure as motor, not like drive.

## Slide 8
Previous Code is here
We should save it and crate new one

## Slide 9
This is newly created one

## Slide 10
We will see different movement blocks
We will select “move motor”

## Slide 11
This is the default version of the motor block. We should change and customize it.

## Slide 12
Our motor is in third port that why we are changing the “motor1” to “motor3”.

## Slide 13
This section determine the rotating direction of the motor. In our case we should change it to “reversed”. In this case our mechanism will lif.

## Slide 14
This part of the motor block we write the operation time of the motor. In the first case, “1” will be tested.

## Slide 15
This section defines the speed of motor. It should be decreased to “34 rpm”. Higher speed can lead to unstable movement of the scissor mechanism.

## Slide 16
Great! We can test our code at this moment.
After running the code, scissor mechanism should rise..

## Slide 17
After rising the scissor mechanism, we should drop it. That is why the direction of the movement should be changed from “reversed” to “forward”

## Slide 18
Second motor block has been added to supply drop movement. Before testing the code, we should customize it.
Now, we will write a code which will rise and drop the scissor mechanism.

## Slide 19
After changing important point, our code is ready for test!

## Slide 20
In this step, we will apply “wait” block. Main task of this block is to pause during defined time and continue.
We can find “wait” block as shown in left!

## Slide 21
We can increase or decrease the time to pause out code.

## Slide 22
Now, we will move our robot. We have two motor for movement, and we will use drive block in order to operate two wheel connected motors.

## Slide 23
Speed also can be decreased for stable move.

## Slide 24
To make pause after 3 seconds forward movement, we add wait block.

## Slide 25
We can turn our robot to left with the hep of this “turn” block
We should again decrease the speed